BID PROPOSAL

(SUBMIT IN DUPLICATE)

Having read the Bidding Documents and the Specifications in their entirety, prepared by the Austintown Local School District for said project; the undersigned hereby proposes to furnish all equipment for:

Austintown Local SCHOOL DISTRICT

Fourteen (14) total seventy eight passenger, Propane fueled buses Four (4) units equipped with wheelchair lift and seat belt seat option.

Austintown Local School District will consider bids that will encompass the entire specifications.

SUBMITTED BY:

NAME OF FIRM:

_____________________________________________

STREET ADDRESS:

_____________________________________________

CITY, STATE, ZIP:

_____________________________________________

CONTACT PERSON:

_____________________________________________

PHONE #:

_____________________________________________

FAX #:

_____________________________________________

EMAIL:

_____________________________________________

Minimum Specifications

Complete Unit: 78 Passenger

INSTRUCTIONS:

Column 3: Enter ‘YES’, if Item is included

Column 4: Enter any descriptive or clarification comments, as needed. Add extra sheets, citing Item #, if required.

|  | 2 Description |  |  |  |  | 3­Included? |  | Comments |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | CHASSIS SECTION |  |  |  |  |
|  |  | The air intake and air |  |  |  |  |
|  |  | cleaner shall be readily |  |  |  |  |
|  |  | accessible for servicing. |  |  |  |  |
| 1. | AIR CLEANER | The air cleaner shall |  |  |  |  |
|  |  | include an air restriction |  |  |  |  |
|  |  | indicator. The air filter |  |  |  |  |
|  |  | shall be a heavy duty |  |  |  |  |
|  |  | single stage type. |  |  |  |  |
|  |  | Compressor shall be |  |  |  |  |
|  |  | 13.2 CFM at 2400 RPM |  |  |  |  |
|  |  | minimum and shall be |  |  |  |  |
|  |  | gear driven. All air lines |  |  |  |  |
| 2. | AIR SYSTEM | are to be nylon (or |  |  |  |  |
|  |  | equivalent) and color |  |  |  |  |
|  |  | coded for ease in |  |  |  |  |
|  |  | identification. Air dryer |  |  |  |  |
|  |  | to be included. Total |  |  |  |  |
|  |  | air tank capacity to be |  |  |  |  |
|  |  | 4260 cu. in. |  |  |  |  |
| 3. | ALTERNATOR | Shall be 12 volts; 240 |  |  |  |  |
|  |  | amps minimum |  |  |  |  |
| 4. | AXLES | Front shall be heavy |  |  |  |  |
|  |  | duty 12,000 lbs. full |  |  |  |  |

|  |  |  | power steering. . Rear |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | axle shall be 23,000 |  |  |  |  |  |
|  |  |  | lbs. capacity. Single |  |  |  |  |  |
|  |  |  | speed, oil slinger. |  |  |  |  |  |
|  |  |  | Shall be Three Group |  |  |  |  |  |
|  | 5. | BATTERY | 31, 12 volt, 2100 CCA, |  |  |  |  |  |
|  |  |  | deep cycle, mounted in |  |  |  |  |  |
|  |  |  | a box slide out tray. |  |  |  |  |  |
|  |  |  | Front wheel bearing |  |  |  |  |  |
|  | 6. | BEARINGS | shall be gear oil type, |  |  |  |  |  |
|  |  |  | rear shall be single |  |  |  |  |  |
|  |  |  | speed, oil slinger type. |  |  |  |  |  |
|  |  |  | Dual full air, 16.5x5 |  |  |  |  |  |
|  |  |  | front and 16.5x7 |  |  |  |  |  |
|  |  |  | rear."S" cam, |  |  |  |  |  |
|  | 7. | BRAKES – | Non­asbestos extended |  |  |  |  |  |
|  |  |  | wear |  |  |  |  |  |
|  |  | SERVICE |  |  |  |  |  |  |
|  |  |  | lining. Automatic slack |  |  |  |  |  |
|  |  |  | adjusters. Bendix |  |  |  |  |  |
|  |  |  | AD­IP air dryer. Dust |  |  |  |  |  |
|  |  |  | shields. |  |  |  |  |  |
|  |  | BRAKES ­ | 30 sq. in. spring brake |  |  |  |  |  |
|  | 8. |  | with treadle valve. |  |  |  |  |  |
|  |  | EMERGENCY. | Separate valve for |  |  |  |  |  |
|  |  |  | parking, E­Z grip cover |  |  |  |  |  |
|  |  |  | Circuit protection shall |  |  |  |  |  |
|  |  |  | be automatically |  |  |  |  |  |
|  |  |  | resetting circuit |  |  |  |  |  |
|  |  |  | breakers. All wiring |  |  |  |  |  |
|  |  |  | shall be color coded |  |  |  |  |  |
|  | 9. | ELECTRICAL | and numbered. |  |  |  |  |  |
|  |  |  | Complete schematics |  |  |  |  |  |
|  |  |  | shall be provided with |  |  |  |  |  |
|  |  |  | each bus. Two spare |  |  |  |  |  |
|  |  |  | wires running to the |  |  |  |  |  |
|  |  |  | rear of the bus for future |  |  |  |  |  |
|  |  |  | use. |  |  |  |  |  |

|  |  |  | 6.8 Liter, Liquid |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 10. | ENGINE | propane autogas fuel |  |  |  |  |  |
|  |  |  | system. Dual fuel |  |  |  |  |  |
|  |  |  | pumps mounted |  |  |  |  |  |
|  |  |  | inside the fuel tank. |  |  |  |  |  |
|  | 11. | EXHAUST | Tail pipe to exit ahead |  |  |  |  |  |
|  |  |  | of left side dual rear |  |  |  |  |  |
|  |  |  | wheels. |  |  |  |  |  |
|  |  |  | Fuel systems using |  |  |  |  |  |
|  |  |  | liquefied petroleum gas |  |  |  |  |  |
|  |  |  | (LPG) shall comply with |  |  |  |  |  |
|  | 12. | FUEL SYSTEM | the NFPA Standard 58 |  |  |  |  |  |
|  |  |  | “Liquefied Petroleum |  |  |  |  |  |
|  |  |  | Gases Engine Fuel |  |  |  |  |  |
|  |  |  | Systems” in effect at |  |  |  |  |  |
|  |  |  | the time of installation. |  |  |  |  |  |
|  |  |  | Shall include |  |  |  |  |  |
|  |  |  | speedometer with |  |  |  |  |  |
|  |  |  | seven digit odometer, |  |  |  |  |  |
|  |  |  | amp meter, |  |  |  |  |  |
|  |  |  | tachometer, hour |  |  |  |  |  |
|  |  |  | meter, gauges for oil |  |  |  |  |  |
|  |  |  | pressure, coolant |  |  |  |  |  |
|  |  |  | temperature, |  |  |  |  |  |
|  |  |  | transmission |  |  |  |  |  |
|  |  |  | temperature, voltage, |  |  |  |  |  |
|  | 13. | INSTRUMENTS | and dual air pressure |  |  |  |  |  |
|  |  |  | gauges. Audio/visual |  |  |  |  |  |
|  |  |  | warning system for low |  |  |  |  |  |
|  |  |  | oil pressure, high |  |  |  |  |  |
|  |  |  | coolant temperature, |  |  |  |  |  |
|  |  |  | and low air pressure. |  |  |  |  |  |
|  |  |  | Headlights “left on” |  |  |  |  |  |
|  |  |  | warning chime. |  |  |  |  |  |
|  |  |  | Warning system must |  |  |  |  |  |
|  |  |  | not shut down engine. |  |  |  |  |  |
|  |  |  | Digital clock, dash |  |  |  |  |  |
|  |  |  | mounted and resettable |  |  |  |  |  |

|  |  |  | trip odometer. Horn, |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | electric, dual tone. |  |  |  |  |  |
|  | 14. | KEYS | Key type start and stop |  |  |  |  |  |
|  |  |  | switch. Dash mounted |  |  |  |  |  |
|  |  |  | transmission shifter. |  |  |  |  |  |
|  | 15. | MANUALS | Complete maintenance |  |  |  |  |  |
|  |  |  | and parts manuals shall |  |  |  |  |  |
|  |  |  | be provided with bus. |  |  |  |  |  |
|  |  |  | Front and rear shall be |  |  |  |  |  |
|  | 16. | SHOCKS | heavy duty, direct |  |  |  |  |  |
|  |  |  | acting double action |  |  |  |  |  |
|  |  |  | piston type. |  |  |  |  |  |
|  |  |  | Steering column shall |  |  |  |  |  |
|  |  |  | include tilt and |  |  |  |  |  |
|  | 17. | STEERING | telescope. Pump shall |  |  |  |  |  |
|  |  |  | be gear driven. |  |  |  |  |  |
|  |  |  | Electronic cruise |  |  |  |  |  |
|  |  |  | control. Adjustable |  |  |  |  |  |
|  |  |  | high idle switch |  |  |  |  |  |
|  |  |  | Front: Parabolic springs |  |  |  |  |  |
|  | 18. | SUSPENSION | 10,000 lbs. Rear: Air |  |  |  |  |  |
|  |  |  | ride 23,000 lbs. |  |  |  |  |  |
|  |  |  | capacity. |  |  |  |  |  |
|  | 19. | TIRES | 11R 22.5, 14 ply radial |  |  |  |  |  |
|  |  |  | tubeless tires.All rear |  |  |  |  |  |
|  |  |  | tires lug type |  |  |  |  |  |
|  | 20. | TRANSMISSION | Automatic |  |  |  |  |  |
|  |  |  | Minimum requirements: |  |  |  |  |  |
|  | 21. | WARRANTY | ­­ Chassis two (2) year |  |  |  |  |  |
|  |  |  | 24,000 miles; |  |  |  |  |  |
|  |  |  | ­­ Engine five (5) years |  |  |  |  |  |
|  |  |  | 100,000 miles; |  |  |  |  |  |

|  |  |  | ­­ Transmission five (5) |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | year unlimited miles. |  |  |  |  |  |
|  |  |  | (Optional extend |  |  |  |  |  |
|  |  |  | warranty will be |  |  |  |  |  |
|  |  |  | considered.) |  |  |  |  |  |
|  | 22. | WHEELS | 10 Stud disc type, |  |  |  |  |  |
|  |  |  | hub­piloted, 22.5 x |  |  |  |  |  |
|  |  |  | 8.25. |  |  |  |  |  |  |
|  | 23. | WHEELBASE | Maximum of 280", curb |  |  |  |  |  |
|  |  |  | turning radius not to |  |  |  |  |  |
|  |  |  | exceed 35.3 feet. |  |  |  |  |  |
|  | 24. | TOW HOOKS | Bus shall be supplied |  |  |  |  |  |
|  |  |  | with front and rear tow |  |  |  |  |  |
|  |  |  | hooks. |  |  |  |  |  |

|  | 1 |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | Ite | 2 Specification |  |  |  |  | 3 Included? |  | 4 Comments |  |
|  | m |  |  |  |  |  |  |  |  |  |
|  |  |  |  | BODY SECTION |  |  |  |  |  |
|  |  |  | Enclosed compartment with |  |  |  |  |  |
|  | 1. | BATTERY COMP | sliding tray. Tray to be held |  |  |  |  |  |
|  |  |  | in place with a retaining pin. |  |  |  |  |  |
|  |  |  | Door hinged at the side with |  |  |  |  |  |
|  |  |  | a recessed handle. |  |  |  |  |  |
|  |  |  | Front and rear, plate steel, |  |  |  |  |  |
|  |  |  | one piece, die­formed. |  |  |  |  |  |
|  |  |  | Frame mounted, front and |  |  |  |  |  |
|  | 2. | BUMPERS | rear |  |  |  |  |  |
|  |  |  | at least 12" in height. Front |  |  |  |  |  |
|  |  |  | bumper to include a plate |  |  |  |  |  |
|  |  |  | with a white reflective |  |  |  |  |  |
|  |  |  | background for placement |  |  |  |  |  |
|  |  |  | of State ID number. |  |  |  |  |  |
|  |  |  | Four rub rails to be applied |  |  |  |  |  |
|  |  |  | to exterior side panels. |  |  |  |  |  |
|  |  |  | Positions shall be at bottom |  |  |  |  |  |
|  |  |  | of window edge, at seat |  |  |  |  |  |
|  |  |  | level, at floor level, and at |  |  |  |  |  |
|  |  |  | the bottom of the side |  |  |  |  |  |
|  |  |  | panel. Shall be painted |  |  |  |  |  |
|  | 3. | CONSTRUCTION | black. 16 gauge side panels |  |  |  |  |  |
|  |  |  | 15­½” skirt. Colorado rack |  |  |  |  |  |
|  |  |  | test compliant. Full length |  |  |  |  |  |
|  |  |  | bows from floor line to floor |  |  |  |  |  |
|  |  |  | line. Roof bows not to |  |  |  |  |  |
|  |  |  | extend below floor. Rain |  |  |  |  |  |
|  |  |  | visors over side windows to |  |  |  |  |  |
|  |  |  | be embossed in roof panels |  |  |  |  |  |
|  |  |  | to reduce seams. |  |  |  |  |  |
|  | 4. | CROSS ARM | Air operated bumper |  |  |  |  |  |
|  |  |  | mounted crossing gate. |  |  |  |  |  |

|  |  |  | To be 90,000 BTU |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | minimum. Windshield to |  |  |  |  |  |
|  |  |  | have full length defroster |  |  |  |  |  |
|  | 5. | DEFROSTERS | channel to supply even |  |  |  |  |  |
|  |  |  | defrosting. Two auxiliary |  |  |  |  |  |
|  |  |  | fans mounted on dash so |  |  |  |  |  |
|  |  |  | as not to work against |  |  |  |  |  |
|  |  |  | defrosters. |  |  |  |  |  |
|  |  |  | 6­Way adjustable. Air |  |  |  |  |  |
|  |  |  | suspension, high­back, |  |  |  |  |  |
|  |  |  | vinyl upholstery with a foam |  |  |  |  |  |
|  |  |  | seat cushion and back, |  |  |  |  |  |
|  | 6. | DRIVER SEAT | entire seat to be adjustable |  |  |  |  |  |
|  |  |  | without tools. Adjustable, |  |  |  |  |  |
|  |  |  | orange driver’s shoulder belt |  |  |  |  |  |
|  |  |  | required. Storage pouch to |  |  |  |  |  |
|  |  |  | be furnished behind driver’s |  |  |  |  |  |
|  |  |  | seat. |  |  |  |  |  |
|  |  |  | Two halogen headlights, |  |  |  |  |  |
|  |  |  | daytime running lights. |  |  |  |  |  |
|  |  |  | Shall be ten (10) interior |  |  |  |  |  |
|  | 7. | LIGHTS | overhead lights with clear |  |  |  |  |  |
|  |  |  | plastic lens. Driver’s dome |  |  |  |  |  |
|  |  |  | light with separate switch. |  |  |  |  |  |
|  |  |  | Rheostat dash dimmer on |  |  |  |  |  |
|  |  |  | headlight switch |  |  |  |  |  |
|  |  |  | Warning lights system |  |  |  |  |  |
|  |  |  | meeting current State |  |  |  |  |  |
|  | 8. | LIGHTS ­ WARNING | specifications and hooded |  |  |  |  |  |
|  |  |  | to improve visibility. LED |  |  |  |  |  |
|  |  |  | marker lights, flush |  |  |  |  |  |
|  |  |  | mounted. Low profile strobe |  |  |  |  |  |
|  |  |  | light. |  |  |  |  |  |
|  |  |  | Rear door, located to have |  |  |  |  |  |
|  | 9 | EMERGENCY | grease­able strap hinges |  |  |  |  |  |
|  |  |  | and a positive retainer to |  |  |  |  |  |
|  |  |  | hold door open |  |  |  |  |  |

|  |  |  | Entrance door to be |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | outward opening. Shall |  |  |  |  |  |
|  | .10. | ENTRANCE | have grease­able hinges |  |  |  |  |  |
|  |  |  | and be air operated. Grab |  |  |  |  |  |
|  |  |  | rails to be located on both |  |  |  |  |  |
|  |  |  | sides and have a vandal |  |  |  |  |  |
|  |  |  | lock. |  |  |  |  |  |
|  |  |  | Four (4) push out |  |  |  |  |  |
|  |  |  | emergency exit windows, |  |  |  |  |  |
|  |  |  | two per side. Two window to |  |  |  |  |  |
|  |  |  | be located on opposite |  |  |  |  |  |
|  |  |  | sides in the front ⅓ of the |  |  |  |  |  |
|  |  |  | unit. Two windows to be |  |  |  |  |  |
|  | 11. | EXITS | located opposite of each |  |  |  |  |  |
|  |  |  | other in the rear ⅓ of the |  |  |  |  |  |
|  |  |  | unit. Seat backs not to |  |  |  |  |  |
|  |  |  | interfere with escape route |  |  |  |  |  |
|  |  |  | through window. Two (2) |  |  |  |  |  |
|  |  |  | roof mounted combination |  |  |  |  |  |
|  |  |  | vent/escape hatches, |  |  |  |  |  |
|  |  |  | evenly spaced. |  |  |  |  |  |
|  | 12. | FLOOR | Marine grade plywood |  |  |  |  |  |
|  |  |  | installed over steel floor, |  |  |  |  |  |
|  |  |  | fastened with screws. |  |  |  |  |  |
|  |  |  | Windshield: Two­piece |  |  |  |  |  |
|  |  |  | curved, shaded, and |  |  |  |  |  |
|  |  |  | bonded. Assist handles |  |  |  |  |  |
|  |  |  | installed above the |  |  |  |  |  |
|  |  |  | windshield to facilitate |  |  |  |  |  |
|  | 13. | GLASS | cleaning. |  |  |  |  |  |
|  |  |  | Tinted Glass: |  |  |  |  |  |
|  |  |  | ­­ Side windows ­ 28%; |  |  |  |  |  |
|  |  |  | ­­ Entrance door ­ 70%; |  |  |  |  |  |
|  |  |  | ­­ Driver’s window ­ 70%. |  |  |  |  |  |
|  | 14. | HEATERS & FANS | All heaters are required to |  |  |  |  |  |
|  |  |  | have cleanable filters. |  |  |  |  |  |

|  |  |  | Heater cutoff valves to be |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | ball type ¼ turn shutoff. |  |  |  |  |  |
|  |  |  | ­­ Right front heater: 90,000 |  |  |  |  |  |
|  |  |  | BTU; three (3) speeds, with |  |  |  |  |  |
|  |  |  | defroster for entrance door |  |  |  |  |  |
|  |  |  | and windshield. |  |  |  |  |  |  |
|  |  |  | ­­ Driver’s heater: | 12,000 |  |  |  |  |  |
|  |  |  | BTU. |  |  |  |  |  |  |
|  |  |  | ­­ Mid­ship heater: | 80,000 |  |  |  |  |  |
|  |  |  | BTU with dual two (2) speed |  |  |  |  |  |
|  |  |  | fans. |  |  |  |  |  |  |
|  |  |  | ­­ Rear heater: 80,000 BTU |  |  |  |  |  |
|  |  |  | located behind wheelhouse |  |  |  |  |  |
|  |  |  | with dual two (2) speed |  |  |  |  |  |
|  |  |  | fans. |  |  |  |  |  |  |
|  |  |  | Insulation located in the |  |  |  |  |  |
|  |  |  | ceiling and side walls with |  |  |  |  |  |
|  | 15. | INSULATION | additional insulation in |  |  |  |  |  |
|  |  |  | driver's area. All ceiling |  |  |  |  |  |
|  |  |  | panels to be perforated to |  |  |  |  |  |
|  |  |  | reduce engine noise (full |  |  |  |  |  |
|  |  |  | length acoustic headliner). |  |  |  |  |  |
|  | 16. | INTERIOR | Side panels shall be |  |  |  |  |  |
|  |  |  | anodized aluminum from |  |  |  |  |  |
|  |  |  | windows to seat rail. |  |  |  |  |  |
|  | 17. | MANUALS | Complete maintenance and |  |  |  |  |  |
|  |  |  | parts manuals on disc shall |  |  |  |  |  |
|  |  |  | be provided with bus. |  |  |  |  |  |
|  |  |  | Interior, rearview 6” x 30” |  |  |  |  |  |
|  |  |  | non­glare, sun visor 6” x 30” |  |  |  |  |  |
|  |  |  | Plexiglas. All exterior |  |  |  |  |  |
|  | 18. | MIRRORS | mirrors heated with 15 |  |  |  |  |  |
|  |  |  | minute timer, and side |  |  |  |  |  |
|  |  |  | mirrors remote control, |  |  |  |  |  |
|  |  |  | open view. Stainless steel |  |  |  |  |  |
|  |  |  | mirror brackets. |  |  |  |  |  |  |

|  | 19. | MUD FLAPS | Front mud flaps & rear flap |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | full width of bus located |  |  |  |  |  |
|  |  |  | right behind rear wheels. |  |  |  |  |  |
|  |  |  | Engine compartment, step |  |  |  |  |  |
|  |  |  | well, and firewall to have |  |  |  |  |  |
|  |  |  | deluxe sound deadening |  |  |  |  |  |
|  |  |  | package. All unexposed |  |  |  |  |  |
|  | 20. | NOISE | interior surfaces except |  |  |  |  |  |
|  |  |  | ceiling, to have sprayed­on |  |  |  |  |  |
|  |  |  | sound deadening material |  |  |  |  |  |
|  |  |  | applied prior to assembly. |  |  |  |  |  |
|  |  |  | Interior to have full length |  |  |  |  |  |
|  |  |  | beige acoustic panel. |  |  |  |  |  |
|  |  |  | Painted interior panels shall |  |  |  |  |  |
|  |  |  | be baked on enamel. Color |  |  |  |  |  |
|  | 21. | PAINT | shall be beige. Exterior, |  |  |  |  |  |
|  |  |  | heat cured. Polyurethane |  |  |  |  |  |
|  |  |  | white roof. Exterior to have |  |  |  |  |  |
|  |  |  | 3M reflector system. |  |  |  |  |  |
|  |  |  | All required equipment to |  |  |  |  |  |
|  | 22. | SAFETY EQUIPMENT | State specifications shall |  |  |  |  |  |
|  |  |  | be supplied and mounted in |  |  |  |  |  |
|  |  |  | overhead compartment. |  |  |  |  |  |
|  |  |  | Seat back shall not interfere |  |  |  |  |  |
|  |  |  | with using emergency |  |  |  |  |  |
|  | 23. | SEATS ­ PASSENGER | window exits. Seats shall |  |  |  |  |  |
|  |  |  | be brown, 39” wide. Seat |  |  |  |  |  |
|  |  |  | cushions to have plywood |  |  |  |  |  |
|  |  |  | bottoms. |  |  |  |  |  |
|  |  |  | All exterior service access |  |  |  |  |  |
|  | 24. | SERVICE ACCESS | doors must be lockable and |  |  |  |  |  |
|  |  |  | keyed­alike. Tilt hood with |  |  |  |  |  |
|  |  |  | low effort assist ( 20 lb. |  |  |  |  |  |
|  |  |  | maximum ). |  |  |  |  |  |
|  |  |  | AM/FM CD/Clock with |  |  |  |  |  |
|  | 25. | SOUND | interior/exterior PA. Eight |  |  |  |  |  |
|  |  |  | (8) interior­mounted heavy |  |  |  |  |  |
|  |  |  | duty speakers. One of the |  |  |  |  |  |

|  |  |  | speakers to be mounted in |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | driver’s area.System to be |  |  |  |  |  |
|  |  |  | wired into the noise kill |  |  |  |  |  |
|  |  |  | switch. |  |  |  |  |  |
|  | 26. | STEP WELL | Three step, non­skid, rubber |  |  |  |  |  |
|  |  |  | covered steps constructed |  |  |  |  |  |
|  |  |  | of stainless steel. |  |  |  |  |  |
|  | 27. | STOP ARM | Stop arm to be air­operated |  |  |  |  |  |
|  |  |  | with LED lights. |  |  |  |  |  |
|  |  |  | All accessory switches: |  |  |  |  |  |
|  |  |  | heaters, warning lights, etc. |  |  |  |  |  |
|  |  |  | must be mounted on a |  |  |  |  |  |
|  |  |  | separate panel located just |  |  |  |  |  |
|  | 28. | SWITCH PANEL | below the driver’s window or |  |  |  |  |  |
|  |  |  | on the right side dash area |  |  |  |  |  |
|  |  |  | and placed within easy |  |  |  |  |  |
|  |  |  | reach of the driver. Must |  |  |  |  |  |
|  |  |  | have a cutoff switch for |  |  |  |  |  |
|  |  |  | interior noise (i.e. |  |  |  |  |  |
|  |  |  | railroad/quiet switch). |  |  |  |  |  |
|  |  |  | Before mounting on |  |  |  |  |  |
|  | 29. | UNDERCOATING | chassis, unit to be fully |  |  |  |  |  |
|  |  |  | coated and baked­on |  |  |  |  |  |
|  |  |  | undercoating. |  |  |  |  |  |
|  | 30. | WIPERS | Dual electric, bottom |  |  |  |  |  |
|  |  |  | mounted, wet arm, |  |  |  |  |  |
|  |  |  | intermittent operation |  |  |  |  |  |

Four ( 4 ), of the buses will be equipped with the following items

Wheelchair lift Braun L919FIB or equal located right rear. Please submit seat plan.

Wheelchair restraint, Q'Straint QRT­Max or equal.

Track mounted seats which can be removed for future wheelchair use.

Optional. Seat belt seat option for Four buses with lifts

Please provide separate sheets for these units

| Wheelchair lift | cost | Comments |
| --- | --- | --- |

Q'Straint QRT­Max or

equal.

Seat belt seat option for

buses with lifts.

Please submit seat plan

for three wheelchair

accommodations

UNIT PRICE includes

All Items as confirmed in the Minimum Specifications for the Chassis (pages B, C & D) and Body (pages E, F, G, & H)

- Vehicle(s) delivered to:

∙

Austintown Local Schools

Attn: Colleen Murphy­Penk

Transportation Department

275 Idaho Rd.

Youngstown, Ohio 44515

UNIT PRICE:

Written Amount  _________________________________________________________dollars

Dollar Amount

$__________________

Estimated Build & Delivery Lead­time:	________________________ months

(no later than on or before August 1, 2014)

Please note where warranty work will be completed:

_____________________________________________________

_____________________________________________________

_____________________________________________________

Bidder hereby agrees to deliver equipment prior to or no later than August 1, 2014.

Acknowledgment of Addenda (if applicable):

Addenda Number	Signature

Date

#

#

#

It is understood and agreed that the ALS District reserves the right to waive any informalities, or to accept/reject any part or all of any bid submitted, and that this proposal may not be withdrawn for a period of sixty (60) days subsequent to the bid opening without permission of the ALS District.

The undersigned agrees to execute a Contract for the above proposal for a compensation computed above. All conditions and provisions of the Bid Document are deemed to be accepted by the Vendor and will be incorporated into the contract.

____________________________________________ Name

___________________________

Title

____________________________________________ Signature

___________________________

Date

SUBSTITUTION SHEET

Bidder shall list any "Approved Substitutes" included in the bid. Only substitutions communicated and approved via Bid Document Addenda are permitted. A Bidder utilizing the approved substitution must incorporate the cost of said substitution in their vehicle bid.

If this page is not completed, the Austintown Local School District will understand the bid adheres exactly to the specifications.

| Item # | Description of Approved Substitution |  |
| --- | --- | --- |
| ______ | ______________________________________________________________________________________ |
| ______ | ______________________________________________________________________________________ |
| ______ | ______________________________________________________________________________________ |
| ______ | ______________________________________________________________________________________ |
| ______ | ______________________________________________________________________________________ |
| ______ | ______________________________________________________________________________________ |
| _________________________________ | _______________ |
| Bidder | Signature | Date |