Project Scope and Requirements

I.	Introduction	1

II.	General Information	2

III.	Summary of Important Dates:	2

IV.	Proposal Preparation and Format Requirements	3

V.	Selection Process and Basis of Award	3

VI.	Scope of Work	4

A.	Cameras	4

B.	Mounting Hardware	5

C.	Recording System	5

D.	Viewing Station, Room C100(Security Office)	5

E.	Rack System, Room C200	6

F.	Installation	6

G.	Training	7

H.	Maintenance	7

VII.	Appendices	8

Appendix 1 – Price Sheet	9

# Introduction

Oakton Community College seeks to enrich student experience in all facets.  Paramount to an environment conducive to educating members of the community is the safety of students, faculty and staff.  Oakton Community College presents this Request for Proposals to solicit a digital video surveillance system for its Ray Hartstein Campus in Skokie, Illinois which meets current surveillance needs, provides the opportunity for expansion in the future, and is compatible with College systems already in place.

Oakton Community College is soliciting proposals from firms with demonstrated experience in installing and maintaining video surveillance, storage systems and display infrastructures.

Qualified interested firms should obtain the detailed Request for Proposals package on the College’s website at www.oakton.edu.  Additional information concerning directions to accessing proposal through the internet and webpage is found in the business section of this proposal.

The closing date and time for receipt of proposals is 11:00AM prevailing time (CDT) on Tuesday, July 10, 2007, after which time proposals will not be accepted.

# General Information

Oakton Community College requests proposals to provide and install Panasonic video surveillance cameras and rack mounted recording hardware and software as specified.  This solicitation is designed to completely replace the system currently in place and provide a turnkey solution for the College.  All cameras will be wired using plenum siamese cable which will be purchased separately and installed by College.  Wiring to camera locations is not a part of this Request for Proposals, although termination at both the individual camera and head end locations should be considered part of this solicitation.  By law contractors will be required to pay their workers prevailing wages/union scale for this project and submit appropriate paperwork concerning this requirement.

This Request for Proposals asks prospective vendors to quote only the equipment and manufacturers provided herein.  Substitutions will not be accepted.

Inquiries about the RFP, questions raised at the pre-proposal meeting and our responses will be distributed to all participating companies the week of July 2, 2007.

# Summary of Important Dates:

1.	Thursday, June 21, 2007, proposals are ready for distribution.

2.	Wednesday, June 27, 2007, mandatory pre-proposal meeting at 9:30AM in Room B204 at the Ray Hartstein Campus, 7701 N. Lincoln Avenue, Skokie, IL 60077.

3.	Tuesday, July 10, 2007 at 11:00AM, proposals are opened in Room 1540, Des Plaines Campus, 1600 E. Golf Road, Des Plaines, IL 60016.

4.	Monday, July 16, 2007 purchase order issued for project.

5.	Monday, July 30, 2007, work begins on the project.

6.	Friday, August 10, 2007, work completed.

7.	Punchlist and training completed week of August 13th.

8.	Monday, August 20, 2007, project 100% completed.

# Proposal Preparation and Format Requirements

Company Information

Provide a brief summary of the firm submitting the proposal as well as any subcontractors who may be used in the completion of this project.  Include a statement from both the proposing firm and from any subcontractors indicating acceptance of the Insurance Requirements and the Terms and Conditions for the project.  The letters must be signed by an individual from the proposing and subcontracting firms authorized to bind each company to this contract.  Payment and performance bonds from a company rated A-/6 by Best will be required for this project.

Scope of Services

Provide an executive summary and schedule confirmation of the proposed products and services to be provided.

Indicate the employee who will be the Project Manager for the duration of this project.

Pricing

Provide an itemized price list (Appendix 1) for all materials included as the base portion of this RFP.  All services should be itemized as well, including installation, testing and base warranty period.  Each alternate item concerning service for this project should be listed separately.

References

Include at least three references of work performed by the contracting firm that are similar in scope and size.

# Selection Process and Basis of Award

Members of the selection committee will review all proposals submitted.  Appropriate finalist(s) will be interview by the selection committee, after which a selection will be made.

The College reserves the right to reject any proposals.

The College will evaluate submitted proposals on the following criteria:

- Price

- Compliance with Requirements

- References

Additional criteria:

- Ability and skill of the firm to meet the requirements of the RFP and provide continued support and maintenance.

- Ability to provide products and services in the timeframe specified in this RFP without delay.

# Scope of Work

Note 1: The system specifications call for a Digital Video Surveillance (DVR) solution with analog cameras.  Although video surveillance is moving from analog to Internet Protocol (IP) cameras, Oakton Community College feels migrating directly to an IP-based solution is cost-prohibitive at this time.  The cost of an eventual migration to an IP-based system can be mitigated by purchasing an analog solution with architecture allowing the College to easily add, change or remove elements of the surveillance system as upgrades are required.

Note 2: All products listed plus 1 year of continued service and regular maintenance are to be included in the base bid.  Alternate Bid A should include the cost of continued service and regular maintenance for 2 years and Alternate Bid B should include the cost of continued service and regular maintenance for 3 years (see Section VI, I.).

### Cameras

All camera locations are indicated on the map attached to this RFP.  Winning contractor will verify camera locations with owner before installation.

- Five (5) Panasonic WV-CW964 Weather Proof Super Dynamic III Color Dome Cameras

Minimum Requirements

| Power Requirements | 24V AC, 60Hz |
| --- | --- |
| Image Sensor | ¼” interline transfer CCD |
| Effective Pixels | 768(H) x 494(V) |
| Minimum Illumination | Day/Night Function 0.5 lux color mode/0.04 lux black and white mode |
| Resolution | Horizontal: 480 TVL minimum (color normal mode) 540 TVL typical; 520 TVL minimum (color high mode) 570 TVL minimum (black and white) Vertical: 350 TVL minimum |
| Operating Temperature | -40°F to +122°F |
| Water Resistance | IP66 Environmental protection |
| Pan Range | 360° endless pan |
| Tilt Range | -5° to +185° tilt range |
| Iris Range | F1.4 – 22 |
| Zoom | 30x Optical, 10x Digital (300x total) |

- Twenty-nine (29) Panasonic WV-CF284 Color Dome Cameras

Minimum Requirements

| Power Requirements | 12V DC, 220 mA 24V AC, 60 Hz |
| --- | --- |
| Image Sensor | ¼” interline transfer CCD |
| Effective Pixels | 768(H) x 494(V) |
| Minimum Illumination | 0.9 lux |
| Resolution | Horizontal: 540 TVL Vertical: 350 TVL minimum |
| Operating Temperature | 14°F to 122°F |
| Iris Range | F1.4 – 1.8/ 2.8-6mm varifocal lens |

Power Supplies (See Note 3, page 6)

- One (1) 24V AC 8 Output 4 AMP UL Approved Camera Power Supply (for PTZ Cameras only).  Contractor to provide shelf, owner location for installation.

4.	Two (2) Regulated 16 Output 10AMP DC Camera Power Supplies (for Indoor Dome Cameras only).  Contractor to provide shelf, owner location for installation

### Mounting Hardware

- Five (5) Panasonic PWM20GB Wall Mount Brackets

Minimum Requirements

| Finish | Beige powder coat finish |
| --- | --- |
| Load Rating | 50 pounds |

### Recording System

- Two (2) Panasonic WJ-HD316A/1000V

Minimum Requirements

| Power Source | 120V AC, 60Hz |
| --- | --- |
| Power Consumption | 80 W |
| Ambient Operating Temp | +5° C to 45°C |
| Ambient Operating Humidity | Less than 90% |
| Dimensions | 16-9/16” (W) x 3-7/16” (H) x 13-3/4” (D), excluding rubber feet and projections |
| Weight | 21 lbs (9.5kg) |
| Video Input/Output Connectors | BNC |
| Cascade Input Connectors | BNC |
| Monitor Output Connectors | BNC (15-pin D-Sub for VGA) |
| Audio Input/Output | RCA Pin |
| Other Connectors | High Speed Serial Interface, 480 Mbps, Full/Half-Duplex RS-485 (RJ-11), RS232C (9-pin D-Sub), 10baseT/100base TX Ethernet Port (RJ-45) |
| Alarm Port | 1-16 Channel Alarm Input/Output, Alarm Recovery Input, Alarm Suspension Input |

### Viewing Station, Room C100 (Security Office)

- One (1) Dell SE197FP 19” Silence Flat Panel LCD Monitor

Minimum Requirements

| Maximum Resolution | 1280 x 1024 |
| --- | --- |
| Dot/Pixel Pitch | 0.294mm |
| Response Time | 8 ms |
| Interface | VGA CHD-15 |
| Image Contrast Ratio | 700:1 |

- One (1) Grandtec GVC1000 Grand Video Console Video to VGA Converter for Dell SE197FP LCD Monitor

Minimum Requirements

| Dimension | 11.2” x 7.5” x 2.5” |
| --- | --- |
| Weight | 2.8 pounds |
| Output | 1024 x 768 |

- One (1) Panasonic WV-CU650 System Controller

Minimum Requirements

| Power Source | 120V AC 60HZ |
| --- | --- |
| Data Output/Input Port | 6-conductor modular jack (RS-485, Full Duplex) x 2 |
| Lens Functions | Yes |
| Pan/Tilt Functions | Yes |
| Ethernet Port | No |
| RS-485 Terminal | Yes |
| Dimensions (HxWxD) | 4.375” x 11.4375” x 8.6875” |
| Weight | 2.86 lbs. |

### Rack System, Room C200

Note 3: The Rack Mount System will be included on the backup generator for the College.  No UPS systems are required.  Winning firm will provide accurate itemized and total power draw of entire surveillance system.

- One (1) Winsted V8691 Standard Vertical Rack Cabinet

Minimum Requirements

| Size | Functional Size 78.75 in. (45 U) H x 26 in. W Overall Size 87 in. H x 22 9/16 in. W x 28 in. D |
| --- | --- |
| Finish | Dove Grey and Peal Grey baked enamel finish |
| Venting | Vented top. Open Base. No door. |

- One (1) Winsted 68 in 10-Outlet Power Supply with 15AMP Circuit Breaker

### Installation (See Note 2 also)

- Installation of the surveillance system includes camera mounting and focusing, power supply mounting, recording system configuration, rack build and viewing system configuration.  Installation is to be turnkey.

- All camera locations, server locations and power supply locations are to be confirmed with owner prior to installation.

- Three additional ports on an existing system will be available for camera termination into the surveillance system.

- Installation of the cameras shall begin on July 30, 2007 with 100% completion by August 20, 2007.  Payment to winning firm shall not be made until Oakton Community College signs that the work is 100% complete.

- All elements of system and camera installation shall conform to local building codes.

- All elements of system and camera installation shall conform to appropriate OSHA guidelines.

- All products shall have been thoroughly tested for a minimum of 48 hours “burn time” to ensure operability.

- No secure location will be offered for materials during installation.  Winning firm will be responsible for all materials until Oakton Community College signs off on 100% completion.

- Installing firm must clean debris from installation locations daily.  Installing firm will be responsible for removal of debris from the campus.

- All extra cabling shall be in ceilings or wall spaces and bundled in a professional manner.

- Twist-on terminations preferred.

- Old products removed during installation, including cameras, mounting hardware and cabling are property of Oakton Community College and shall be inventoried, appropriately packaged and delivered to the Security Office.

- Installing firm shall not interfere with existing power, telephone, video and data service without express permission from Oakton Community College.

- Lift rental shall be the responsibility of the installing firm.

### Training

- Installing firm shall provide at least two 2-hour training sessions, one each at different shift times, to show usage of the installed and configured system.  Training shall include hands-on training and written documentation for reference for all attendees.

- Comprehensive training shall occur immediately after project installation for system administrators.

- Training shall continue as Oakton Community College requires throughout the warranty period.

- Two copies of equipment manuals, training manuals and all product specification sheets shall be given to the College in labeled and tabbed 3-ring binders.

### Maintenance

- Base Bid

Installing firm will be responsible for 1 year warranty on all products, installation, labor, system configuration and upgrades.  Preventative maintenance including system vacuuming and appropriate OS updates shall be performed no less often than every six months.  A single point of contact for maintenance shall be maintained on file with the College Security Office.  Installing firm shall provide service and/or replacement if necessary for malfunctioning equipment within one business day.

- Alternate Bid A

Include a two-year service agreement which covers all the elements listed in the Service Agreement Base Bid.

- Alternate Bid B

Include a three-year service agreement which covers all the elements listed in the Service Agreement Base Bid.

# Appendices

### A.	Appendix 1 – Price Sheet

B.	Appendix 2 – Map of where cameras will be installed will be distributed at the pre-proposal meeting on Wednesday, June 27, 2007 in Room B204 at the Ray Hartstein Campus, 7701 N. Lincoln Avenue, Skokie, IL 60077.

### Appendix 1 – Price Sheet

Base Bid

|  | Item | Qty | Unit Cost | Total Cost |
| --- | --- | --- | --- | --- |
| 1. | Panasonic WV-CW964 Weather Proof Super Dynamic III Color Dome Camera | 5 |  |  |
| 2 | Panasonic WV-CF284 Color Dome Camera | 29 |  |  |
| 3 | 24V AC 8 Output, Minimum 7 AMP UL Approved Camera Power Supply (for PTZ Cameras only) | 1 |  |  |
| 4 | Fused 16 Output 24V AC Minimum 12.5 AMP Camera Power Supplies (for Indoor Dome Cameras only) | 2 |  |  |
| 5 | Panasonic PWM30GB Parapet Mount Bracket | 5 |  |  |
| 6 | Panasonic WV-CU650 System Controller | 1 |  |  |
| 7 | Dell SE197FP 19” LCD Monitor | 1 |  |  |
| 8 | Grandtec GVC1000 Video to VGA Converter | 1 |  |  |
| 9 | Winsted V8691 Standard Vertical Rack Cabinet | 1 |  |  |
| 10 | 10 Outlet Rack Power Supply Manufacturer and Item # _____________________________ Add any necessary hardware needed to mount rack equipment. | 1 |  |  |
| 11 | Installation per specification | 1 |  |  |
| 12 | Training per specification | 1 |  |  |
| 13 | Maintenance – 1 Year per specification | 1 |  |  |

Alternate Bid A

| 14 | Maintenance – 2 Year per specification | 1 |  |  |
| --- | --- | --- | --- | --- |

Alternate Bid B

| 15 | Maintenance – 3 Year per specification | 1 |  |  |
| --- | --- | --- | --- | --- |

Base Bid Total Cost: $ _____________________._______ (numeric)

______________________________________________________________________________(written)

Alternate Bid A Total Cost: $ _____________________._______ (numeric)

______________________________________________________________________________(written)

Alternate Bid B Total Cost: $ _____________________._______ (numeric)

__________________________________________ ___________________________________________________(written)

Name: (Print)______________________________________________

Signature: ________________________________________________

Title: ____________________________________________________

Date: ____________________________________________________