| STATE OF CALIFORNIA • DEPARTMENT OF TRANSPORTATION |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| CHANGE ORDER |  |  | Sheet |  | 1 | of | 2 |
| CEM-4900 (REV 05/2015) | Change Requested by: |  |  |  |  |  |
|  |  |  |  |  | Engineer |  | Contractor |
| CHANGE ORDER NO. | SUPPL. NUMBER | CONTRACT NUMBER | CO-RTE-PM |  | FEDERAL NUMBER(S) |  |  |  |
| 10A |  |  |  |  |  |  |  |  |  |  |

TO

, contractor

You are directed to make the following changes from the plans and specifications or do the following described work not included in the plans and specifications for this contract. NOTE: This change order is not effective until approved by the engineer.

Description of work to be done, estimate of quantities, and prices to be paid. (Segregate between additional work at contract price, agreed price, and force account.) Unless otherwise stated, rates for rental of equipment cover only such time as equipment is actually used and no allowance will be made for idle time. The last percentage shown is the net accumulated increase or decrease from the original quantity in the Bid Item List.

Increases in Bid Items at Bid Item Prices:

At Station 782+32, perform excavation and backfill for the reinforced concrete box culvert shown on Sheet 3 of 3 of this change order.

Item No. 43 (F), Structure Excavation: 220 cf (7%) @ $8.83/cf = $1,942.60 (+18%)

Item No. 44 (F), Structure Backfill: 250 cf (3%) @ $18.85/cf = $4,712.50 (+11%)

Increases in Bid Items at Bid Item Prices = $6,655.10

The quantity increase shown here for Bid Item 43 and Bid Item 44, when combined with quantities shown in the Bid Item List, and as modified by any previous change orders or revisions to dimensions made by the engineer, are the final quantities for which payment is made for each bid item.

Extra Work at Agreed Unit Price:

In accordance with Section 4-1.05, "Changes and Extra Work," of the Standard Specifications, construct a reinforced concrete box culvert at Station 782+32 as shown on Sheet 3 of 3 of this change order and Standard Plans D80, D82, and D83. Perform all work in accordance with Section 51, "Concrete Structures," and Section 52, "Reinforcement," of the Standard Specifications.

A unit price of $216.00 per cubic yard of concrete, measured in accordance with the Standard Specifications, will constitute full and complete compensation, including all markups, for constructing the reinforced concrete box culvert, complete in-place, including all reinforcing steel and incidentals.

Extra Work at Agreed Unit Price = 172 cf @ $216/cf = $37,152.00 increase

This change order does not affect the controlling activity. No time adjustment is warranted.

| ADA Notice | For individuals with sensory disabilities, this document is available in alternate formats. For information, call (916) 445-1233, |
| --- | --- |
|  | TTY 711, or write to Records and Forms Management, 1120 N Street, MS-89, Sacramento, CA 95814. |

| STATE OF CALIFORNIA • DEPARTMENT OF TRANSPORTATION |  |  |  |  |
| --- | --- | --- | --- | --- |
| CHANGE ORDER | Sheet | 2 | of | 2 |
| CEM-4900 (REV 2/2014) |  |  |  |  |
| CHANGE ORDER NO. | SUPPL. NUMBER | CONTRACT NUMBER | CO-RTE-PM | FEDERAL NUMBER(S) |  |  |  |
| 10A |  |  |  |  |  |  |  |

|  |  | Estimated Cost: | Increase | Decrease $ 43,807.10 |
| --- | --- | --- | --- | --- |
| For this order, the time of completion will be adjusted as follows: | None |  |  |  |
| SUBMITTED BY |  |  |  |  |  |
| SIGNATURE | (PRINT NAME AND TITLE) |  |  | DATE |
| APPROVAL RECOMMENDED BY |  |  |  |  |  |
| SIGNATURE | (PRINT NAME AND TITLE) |  |  | DATE |
| ENGINEER APPROVAL BY |  |  |  |  |  |
| SIGNATURE | (PRINT NAME AND TITLE) |  |  | DATE |

We, the undersigned contractor, have given careful consideration to the change proposed and agree to provide equipment, furnish materials, and perform the work specified above, and will accept as full payment the prices shown above. NOTE: If you do not sign this order, you are directed to proceed with the ordered work. You may file a Request for Information within the time specified.

CONTRACTOR ACCEPTANCE BY

SIGNATURE	(PRINT NAME AND TITLE)	DATE